## Slide 1: The Nature of Geographic Data

## Slide 2: Overview
Elaborates on the spatial is special theme
Focuses on how phenomena vary across space and the general nature of geographic variation
Describes the main principles of:
  Spatial variation - spatial autocorrelation
  Scale
  The concept of fractals.

## Slide 3: What is Special about Spatial/Geographic Information (1)?
It is multidimensional (x, y, z)
Large volumes
It may be collected by many different groups, organisations, individuals and needs to be integrated
It may be represented at different resolutions
It must be projected onto a flat surface

## Slide 4: What is Special about Spatial/Geographic Information (2)?
It may be represented in different data structure
It requires specific analysis methods
It requires a range of visualisation methods

## Slide 5: Introduction
Understanding of the ways in which we think about the nature of spatial variation, and ascribe three principles to it:
  that proximity effects are key to understanding spatial variation, and to joining up incomplete representations of unique places;
  that issues of geographic scale and level of detail are key to building appropriate representations of the world;
  that different measures of the world co-vary, and understanding the nature of co-variation can help us with prediction

## Slide 6: Your life…
A digital representation of your life is infinitesimally small compared with the geographic extent and history of the world

## Slide 7: GI is About
Representing spatial and temporal phenomena in the real world
  and, because the real world is complex, this task is difficult and error prone.
Thus,
  Small things (e.g., lives!) are very intricate in detail
  Viewed in aggregate human activity exhibits structure across geographic spaces

## Slide 8: The Fundamental Problem
Must be competent in discarding (or not feeling troubled to measure) the inessentials while retaining the salient characteristics of the observable world
  Distinguishes between controlled variation, which oscillates around a steady state, and uncontrolled variation
    Some applications address controlled variation, such as utility management (daily and weekly patterns)
    Others address uncontrolled, such as those studying longer term processes (e.g. climate change)

## Slide 9: The Fundamental Problem
“Our behavior in space often reflects past patterns of behavior”
  time is one-dimensional, need only look in the past, whereas spatial events can potentially have consequences anywhere in two-dimensional or even three-dimensional space.
How and why does spatial and temporal context affect what we do?
Home vs holiday
Week vs weekend

## Slide 10: Waldo Tobler: First Law of Geography
"Everything is related to everything else,
but near things are more related than distant things.“
[Tobler, 1970, p.236]

## Slide 12: Spatial Autocorrelation
Systematic spatial variation in some phenomena.
Things that are spatially autocorrelated are not randomly distributed through space.
Positive spatial autocorrelation: things that are close together are more likely to be similar
  Socio-economic group.
  Vegetation type.
  Climate.
Negative spatial autocorrelation: things that are close together are more likely to be different
  Examples…?

## Slide 13: Spatial Autocorrelation
Spatial autocorrelation is determined both by similarities in position, and by similarities in attributes
positive, zero, or negative
Lots of different indexes
  Moran’s I
  Geary’s C
  Ripley’s K

## Slide 14
Extreme negative
Extreme positive
Nominal data: blue and white
If features that are similar in location are also similar in attributes, then the pattern as a whole is said to exhibit positive spatial autocorrelation.

## Slide 15: Useful Online Resource:
See a worked example calculation here:
  https://mgimond.github.io/Spatial/spatial-autocorrelation.html

## Slide 16: Spatial Autocorrelation – some issues to consider
Measurement scales and assessment of neighborhood
Issue of sampling intervals
  rhythm of temporal activities and spatial patterning
Self-similarity of spatial and temporal structure
  Extent that patterns are replicated across scales
Coarse scale
Fine scale

## Slide 17: Spatial Autocorrelation and Scale
Understanding of spatial autocorrelation helps us to generalize from sample observations
  becomes easier to build good generalized representations of spatial distributions
Spatial autocorrelation measures attempt to deal simultaneously with similarities in the location of spatial objects and their attributes
Measures of spatial and temporal autocorrelation are scale dependent

## Slide 18: Spatial Autocorrelation and Scale
Understanding scale and spatial structure tell us:
  how we should sample geographic reality
  how we should interpolate between sample observations in order to build representations
Scale, sampling, and interpolation are key to geographic representation

## Slide 19: So, how do we take spatial samples?
Sample frames (Area of interest)
Sampling selects points from a continuous field or, in object case, selects some of these objects while discarding others
Scientific sampling requires that each element in the sample frame has a known and prespecified chance of selection

## Slide 20
Random Sample
Stratified Sample
Stratified
Random Sample
Stratified
Sample with random
variation in grid squares
Clustered Sampling
Sampling along
Transect
Contour Sampling
Spatial sample designs

## Slide 21: Area of Leicestershire
Application-specific sampling to obtain spot heights – may make more observations in hilly terrain where local variation likely to be more heterogeneous
Flat, flood plain
Hilly Terrain
Thus, may be sensible to partition sample frame into sub-areas, based on known spatial structure

## Slide 22
Random Sample
Stratified Sample
Stratified
Random Sample
Stratified
Sample with random
variation in grid squares
Clustered Sampling
Sampling along
Transect
Contour Sampling
Which design would you use for:
Bird sightings
Mineral samples
Voting preferences
Health profiles
Retail distribution

## Slide 23
The coastline of Maine, at three levels of recursion
the base curve of the coastline
(B) approximation using 100-km
steps
(C) 50-km step approximation; and
(D) 25-km step approximation.
Another Kind of Sampling
Different levels are often used at different scales

## Slide 24: Sampling and VGI
More data are collected by other parties rather than for particular purpose
  with the increasing dominance by Big and Open Data
Bias is consequently almost inevitable, and the source and effects of such bias may not be obvious.
Sampling theory tells us that seeking to accommodate the effect of bias is a very dangerous practice.
Volunteered geographic information (VGI)
  It may be possible to invoke automated procedures that are robust and open to scrutiny to ensure that the data provided are unbiased.
E.g. Impact on OpenStreetMap?

## Slide 25: Spatial Interpolation
How to fill in the gaps between our observations?
What is likely attenuating effect of distance between the sample observations?
Identify an appropriate interpolation function

## Slide 26
linear distance decay
(B) negative power distance decay
(C) negative exponential distance decay
Distance Decay

## Slide 27: The Creation of Isopleth Maps
Each graph is regular, continuous, and isotropic
Smooth and continuous variation
  As in isopleth charts
  Isoline – connect equal values
Iso = equal, similar (Greek)
isobar
isohyet
contour

## Slide 28: Example
https://www.topomap.co.nz/

## Slide 29
Choropleth Maps
a spatially extensive variable, total population.
Spatially extensive variables are true of the area as a whole.
(B) a related but spatially intensive variable, population density.
Spatially intensive areas are normalized (densities, ratios, percentages).
Many cartographers would argue that (A) is misleading and that spatially extensive variables should always be converted to spatially intensive form before being displayed as choropleth maps.

## Slide 30: Conclusions
Tobler’s first law of geography
Spatial autocorrelation
  Can be measured by Moran’s I, etc.
Scale & level of geographic detail in a representation
Sampling
Spatial variation can be smooth and continuous, but also can be jagged and irregular